This page was exported from veltak [    http://veltak.is    ]

Export date: Thu Apr 18 6:19:37 2024 / +0000 GMT

## Oil Mist and Machinery Space Fires

Engineroom 2015

Engineroom 2015

Engineroom 2015

### OIL MIST AND MACHINERY SPACE FIRES

### by

### Dr MH Holness PhD, C Chem, FRSC, M Inst Pet. (Petrohaz)

### for

### Quality Monitoring Instruments Ltd Ref. PO 065721 7 June 1995

### Summary

##### A review is presented of the role of oil mist as a principal agent in machinery space fires. The ways in which oil mist can be produced are described and the distinction between mist and spray. The contrast between the oil mist conditions inside crankcases and that in the general atmosphere in machinery spaces is discussed. Methods of measuring oil mist and spray are described and equipment suitable for monitoring conditions inside machinery and in machinery spaces is discussed. Recommendations are made to improve safety on board ship and in industrial plant.

### Contents

#### Introduction

##### Burning of Liquid Fuels

##### Properties of Oil Droplets

##### Crankcase and Gearcase Explosions

##### Fires in Machinery Compartments

##### Oil Drops in the Atmosphere

##### Detection of Oil Mist 5 Conclusions

##### Recommendation

##### References

##### 2

##### 2

##### 3

##### 4

##### 4

##### 4

##### 7

##### 7

##### 8

Oil Mist and Machinery Space Fires

by

### Dr MH Holness (Petrohaz)

### Introduction

A large proportion of machinery space fires have been caused by fuel or lubricant leaks. However,

leaks of this kind, while providing fuel, do not inevitably lead to a fire. In most cases a hot surface of

some kind has produced the conditions necessary to produce flammability and has also acted as

the ignition source. A typical set of circumstances is a leak of fuel from an injector pipe, the fuel falls

onto (say) the turbocharger casing, vaporises and is ignited. This sounds like simple cause and

effect, however there are a series of intermediate stages which ought to be considered.

Burning of Liquid Fuels

Liquid fuels do not burn as liquid, they burn only as vapour. Inevitably, the conversion from liquid to

vapour must require the input of some energy. This can be provided by compression in an engine

or with a hot surface, a spark or a flame.

Outside of an engine or boiler, oil products not usually regarded as "fuel", may also burn under

uncontrolled conditions producing a fire or explosion. Fuel from an injector, under pressure, may

escape as a jet or spray so that it can reach a hot surface. At this point it will vaporise and form a

cloud of vapour expanding away from the heat. As the vapour moves away from the

surface, it cools and re-condenses, forming a cloud of fine mist droplets. During this time, the droplets of fuel near to the hot surface may reach a sufficiently high temperature for spontaneous

ignition to occur and, after a delay period, the whole mist cloud becomes ignited. Similarly, hydraulic

oil from a high pressure line will follow the same mechanism if it contacts a hot surface. The same

process can take place inside machinery, if a mechanical failure occurs creating a high

temperature. This mechanism is well understood and has been described in relation to crankcase

##### explosions in the 1950's (1), and to marine gearbox explosions in the 1970's and 80's (2).

#### Read full text of Article OIL MIST AND MACHINERY SPACE FIRES, Dr MH Holness PhD, C Chem, FRSC, M Inst Pet.

Post date: 2015-10-07 17:12:22

Post date GMT: 2015-04-09 16:45:56

Post modified date: 2016-02-09 13:48:24

Post modified date GMT: 2016-02-09 13:48:24

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com